## Slide 1: Floating-Point Notation
Storing Real numbers since 1985 (2008) (2019)

## Slide 2: Binary Storage
N bits can store integers ranging from 0 to 2N (0 to 2N-1 for signed integers)
Most languages contains 32-bit and 64-bit floats
Python has a 16, 32, or 64-bit float
Side note – Python will automatically assign integers as 32- of 64-bit type

## Slide 3: Binary Storage
Let’s convert the title to the 15th episode of Star Trek: TNG “11001001” to base 10.
How do you represent non-integers?

## Slide 4: Floating-Point Notation
As of 1987, IEEE and ANSI adopted the IEEE-754 standard for floating-point arithmetic
s = one-bit sign
f = fraction (mantissa)
e = exponent
bias = 127 (32-bit), 1023 (64-bit)

## Slide 5: IEEE floating point notation
Sign = stored in 1-bit
Exponent = stored in 8/11 bits
Fraction = stored in 23/52 bits

## Slide 6: Range of Values
32-bit
s = [?]
e (8-bit)= [?]
f (23-bit) = [?]
bias=?
64-bit
s = [?]
e (11-bit)= [?]
f (52-bit) = [?]
bias=?

## Slide 7: Machine Precision
In general
  Single precision is accurate up to 6 decimals
  Double precision is accurate up to 15 decimals
Define machine precision as - the maximum number that can be added to a number without changing the value

## Slide 8: Examples
Represent 7.54
Represent 10-7

## Slide 9: Special Cases
Zero:
  IEEE754 differentiates between -0 and +0
  All bits of exponent and mantissa set to 0
  Sign can be 0 or 1
  Exponent bits all set to 1
  Mantissa bits set to 0
NaN
  Sign can be 0 or 1 (but this is not meaningful for NaN)
  Exponent bits set to 1
  Mantissa bits nonzero